## Slide 1: A Formal language for Critical Human-Machine Interfaces Specification and Validation
Vincent LECRUBIER
PhD Student 2nd year
ONERA, DTIM
Tutors: Bruno d’Ausbourg, Yamine Aït-Ameur

## Slide 2: Overview
Context
Need
Objectives
Approach
Results
Perspectives

## Slide 3: Context: Critical Human Machine Interfaces

## Slide 4: Context: Two clashing domains
Critical Systems
Formal Proof
Model Checking
Static Analysis
Formal Methods
State Machines
Petri Nets
Human-machine Interfaces
Extensive Testing
Usability Analysis
Prototyping
Human Factors
Design
User Feedback
Critical HMIs

## Slide 5: Context: Focus on cockpit HMIs
Thesis
ARINC 661
Man
Cockpit
Display System
User Application
Machine
Actions
Widget Events
Calls
Perception
Parameter Changes
CallBacks

## Slide 6: Problem: A long and costly process
HMI Concept
Textual Specification
HMIs Prototypes
Implemented HMI
Validated HMI
Spécification
Prototyping
Implementation
Validation
Iterations
Non-validation
Long
Costly
Complex
Non reactive

## Slide 7: Objective: Enhance the process
HMI Concept
Formal Specification
Validated HMI
Spécification
Rewriting
Iteration
Traceability
Reactive
Modular
Efficient

## Slide 8: Approach: Outlines
System Engineer
Human Factor Specialist
Coder
Validation Authority
L Specification
Code skeleton
Safety properties checks
Prototype structure
Human factors properties checks

## Slide 9: Approach: Chronology
State of the art
Technology watch
Year1
Year2
Year3
Year4
Language definition
Language formalisation
Test case
Application case
Tooling

## Slide 10: Result: The language
Interactor WXRScreen:
State Variables:
String mode_selection in {"OFF","STDBY","TST","WXON","WXA"}
String tilt_selection in {"AUTO","MANUAL"}
String tilt_stabilization in {"ON","OFF"}
Real tilt_angle in [-15 , 15]
Events:
modeChanged(String newModeSelection)
tiltAngleChanged(Real newTiltAngle)
Components:
TextOutput modeSelectionLabel
TextInput modeSelectionInput
TextOutput tiltSelectionLabel
TriggerInputtiltSelectionButton
TextOutput tiltSelectionValueLabel
TextOutput stabilizationLabel
TriggerInput stabilizationButton
TextOutput stabilizationValueLabel
TextOutput tiltAngleLabel
RealInput tiltAngleInput
Bindings:
modeSelectionLabel.text = "Mode selection:"
modeSelectionInput.text = mode_selection
stabilizationValueLabel.text = tilt_stabilization
stabilizationButton.visible = (tilt_selection != "AUTO")
tiltAngleLabel.value = tilt_angle
Behaviors:
Mode Change
Trigger: modeSelectionInput.inputChanged(newInput)
Guard: none
Effect: mode_selection = newInput; modeChanged(mode_selection)
Tilt angle input by user in manual mode
Trigger: tiltAngleInput.inputChanged(newInput)
Guard: tilt_selection == "MANUAL” && tilt_stabilization == "OFF"
Effect: tilt_angle = newInput; tiltAngleChanged(tilt_angle)

## Slide 11: Results: The language
Interactor
Sub-interactor
Sub-interactor
v1, v2, v3, v4 … vn

## Slide 12: Results: A test case

## Slide 13: Perspectives: Properties to check
Performance
Communication
Temporal properties
Usability
Functionality

## Slide 14: Perspectives
Enhance the language
Extend the language
Tooling
Certification

## Slide 15: Scientific production
Formal H 2012 Workshop, London, UK
http://www.fmhfe.com/FormalH/FormalH.2012.Proceedings.pdf
Appel à projets ANR Blanc 2013
Projet DOLCIA
IHM 2013 Conference, Bordeaux, FR